Solar Panel Power output calculatio Power output calculationn

!!!inverse squarte law
Solar Irradiance

The general answer is the following:
Take the full power output of the Sun (in watts). Divide it by 4π
and divide it by the distance from the sun squared (in metres). They multiply it by the effective area of your solar panels, (if they block each other or are not directly facing the sun, they produce less.), and multiply with the efficiency. You get the power output in watts. Of course, your panels can't convert all the wavelengths the Sun emits, so you might would like to use the luminosity of the Sun only in visible light.

Luminosity = σ * T⁴ * A = constant_boltzmann * Temperatur_sun ⁴ * Area_sun
A = 4* π * Radius_sun ²
Stefan Boltzmann constant	= 5.670367 * 10⁻⁸
sun radius	= 696 342 000 m
sun surface temperatur	= 5700 Kelvin
Power= {L0*A*π*e} over {4*π*r²}= {luminosity_solar * Area_panel * efficiency_panel * π} over {distance_satellite ^2 * 4 * π}
total luminosity solar	= 3.846 x 1026
area	panel	= 1m²
panel efficiency	= 34% (depends on quality)
distance satellite	= variable